## Slide 1
SEMINAR PRESENTATION
Verification Methodologies for RISC-V Processors
A review of how correctness is established for open, extensible processor implementations — with a focus on the base paper: A Self-Testing Framework for a RISC-V-Based System with a Co-processor
Presented by
Kevin Jose
UID: ____________ Class: ____________
Under the guidance of
____________________
Dept. of Computer Science & Engineering
Notes: Fill UID, Class and Guide name before printing.

## Slide 2
AGENDA
1.
Introduction and Objective
2.
Literature Survey — Supporting Papers
3.
Literature Survey — Base Paper
4.
Applications and Relevance
5.
Comparison with Alternate Approaches
6.
Conclusion
7.
References
2

## Slide 3
01 · INTRODUCTION AND MOTIVATION
Introduction and Objective
3
INTRODUCTION
RISC-V is an open, extensible ISA now widely used in academia and industry
Anyone can add custom instructions — but a fabricated processor cannot be patched
Verification establishes that an implementation behaves as its specification requires
THE GAP
The official compliance suite is handwritten and implementation-independent
It cannot target a specific pipeline, hazard logic, or cache configuration
Passing it is not the same as being correct
OBJECTIVE
Review five papers to trace how RISC-V verification has evolved
Understand how each contributes a distinct capability
Show how the base paper applies these to verifying custom instruction-set extensions — the core need of our project
CORE CHALLENGE
Verification normally checks a design against a golden reference. But a custom instruction you invented has no golden reference — and exhaustive testing is impossible (a 32-bit adder alone has 2⁶⁴ input combinations). Every method therefore trades off where tests come from against how correctness is decided.
3

## Slide 4
02 · LITERATURE SURVEY
Five Papers, Five Approaches
4
#
Paper (first author, year)
Core approach
Role
1
χRVFormal — Shen et al., 2026
High-level (Chisel) formal model checking
Supporting
2
RISC-V Vector Accelerator — Jiménez et al., 2023
UVM co-simulation vs Spike golden model
Supporting
3
INSTILLER — Zhang et al., 2024
Coverage-guided RTL fuzzing (ant-colony)
Supporting
4
Polynomial Formal Verif. — Weingarten et al., 2025
BDD equivalence checking, proven time bounds
Supporting
5
PATARA — Gesper et al., 2026
Self-testing (REVERSI), no golden model
Base paper
All five indexed in SCOPUS / SCIE · published 2023–2026 · four journal articles + one Springer journal base paper.
4

## Slide 5
02 · LITERATURE SURVEY — PAPER 1
χRVFormal: Formal Verification of RISC-V Chisel Designs
Shen, Chen, Liu, Zhang, Song & Wu · Journal of Systems Architecture (Elsevier) · 2026
METHODOLOGY
Reference model of RISC-V written in high-level Chisel, not Verilog
Synchronisation mechanism (StateCheck / ActionCheck) aligns a single-cycle model with a pipelined / out-of-order design
Reduces to a model-checking problem solved by Pono / SMTBMC with Boolector
Differs from prior work: verify at the high-level source, not the generated Verilog
KEY FINDINGS
Reference model 4,609 lines vs riscv-formal’s 104,911 — with more coverage
Found 7 real, designer-confirmed bugs; riscv-formal found only 2 of them
Scales to BOOM (out-of-order): 1,953 s avg vs riscv-formal 22,855 s
A bug found in 0.52 s took symbolic execution 58 min
LIMITATIONS
Bounded model checking (depth 40) — not a complete proof
The synchronisation mechanism itself is unverified
Slower than riscv-formal on very small designs
5

## Slide 6
02 · LITERATURE SURVEY — PAPER 2
Functional Verification of a RISC-V Vector Accelerator
Jiménez et al. · IEEE Design & Test · 2023 · European Processor Initiative
METHODOLOGY
UVM testbench with one agent per Open Vector Interface sub-channel (7 total)
Spike ISS as the golden model — every vector instruction co-simulated step by step
50+ SystemVerilog assertions for observability on memory interfaces
Google RISCV-DV for constrained-random generation + Jenkins CI
KEY FINDINGS
3,005 errors found over ~1 year of continuous verification
95.79% functional coverage reached
Ran 24 → 600 tests/night; chip successfully taped out
Memory / narrowing / widening ops = ~70% of failures
LIMITATIONS
Code coverage only 72.64% (49.83% toggle) — authors admit
Targets deprecated RVV 0.7.1, not ratified 1.0
Experience report — engineering, not a new algorithm
6

## Slide 7
02 · LITERATURE SURVEY — PAPER 3
INSTILLER: Toward Efficient and Realistic RTL Fuzzing
Zhang, Wang, Yue, Liu, Guo & Lu · IEEE Trans. CAD of Integrated Circuits & Systems · 2024
METHODOLOGY
Coverage-guided fuzzing: random instruction streams, ISS vs RTL differential check
Ant Colony Optimization (VACO) distills tests — circuits = cities, length = ants
Realistic multi-interrupt and exception injection with priorities
Hardware-aware seed selection and mutation
KEY FINDINGS
+29.4% coverage and +17.0% mismatches vs DiFuzzRTL
Test inputs 79.3% shorter; +6.7% execution speed
Disabling VACO alone → 417% longer inputs (ablation)
Interrupts / exceptions = >10% of coverage prior tools scored 0 on
LIMITATIONS
2 of 4 target cores are OpenRISC, not RISC-V
“Mismatches” are candidate bugs, not designer-confirmed
Fuzzing can never prove the absence of bugs
7

## Slide 8
02 · LITERATURE SURVEY — PAPER 4
Polynomial Formal Verification of a RISC-V Processor
Weingarten, Datta & Drechsler · IEEE Trans. on Nanotechnology · 2025 · Univ. Bremen
METHODOLOGY
Binary Decision Diagrams: canonical form → equivalence = pointer check
Isolate one instruction: pin control signals, mark data unknown, delete constants
Control unit verified as an FSM walk against a golden reference
Novelty: proves a polynomial BOUND on verification time itself
KEY FINDINGS
Proven bounds: O(n) Fetch, O(n²) Execute/Decode, O(k·m) Control
Entire Execute unit verified in 11.95 ms
All 32 control signals verified (up from 15 in prior work)
A complete guarantee — for every possible input
LIMITATIONS
Only MicroRV32 — multi-cycle, NON-pipelined
Excludes HALT, TRAP and interrupt states entirely
Finds zero bugs; closed-source tool
χRVFormal states in print it cannot handle pipelined cores
8

## Slide 9
02 · LITERATURE SURVEY
Supporting Papers — At a Glance
9
Paper
Test generation
Correctness oracle
Headline number
χRVFormal
Exhaustive (formal)
Model checking vs spec
7 real bugs; 4.6k vs 105k LOC
Vector Accelerator
Constrained-random
Spike golden model
3,005 errors; 95.8% func. cov.
INSTILLER
Coverage-guided fuzz
ISS differential
+29% cov; −79% test length
PFV
Exhaustive (formal)
BDD equivalence
O(n²); Execute unit 11.95 ms
TAKEAWAY
Every supporting paper depends on a reference model or an exhaustive proof. The base paper removes that dependency entirely — which is exactly why it was chosen.
9

## Slide 10
03 · LITERATURE SURVEY — BASE PAPER
PATARA: A Self-Testing Framework
Gesper, Stuckmann, Wöbbekind & Payá-Vayá · Int. Journal of Parallel Programming (Springer) · 2026
10
OBJECTIVE
Generate self-checking tests — with no external golden model
Cover implementation-specific hazards the compliance suite misses
Extend verification to an attached co-processor
MAIN CONTRIBUTIONS
REVERSI self-test generation ported to RISC-V
Pipeline hazard-sequence generator (pipeline-depth aware)
Operand swapping + cache-miss generation
Twin-based co-processor verification
HEADLINE RESULT
79.12% → 100%
condition coverage vs the official compliance suite. The suite found 0 bugs — PATARA exposed real hazard bugs in that same "verified" core.
PIPELINE
PATARA
→
REVERSI
self-tests
→
Hazard +
cache gen
→
Twin
co-proc
10

## Slide 11
03 · BASE PAPER
The Problem Being Addressed
11
THE NAIVE APPROACH
Run the handwritten RISC-V compliance suite
Same implementation-independent tests for every core
Cannot target your pipeline depth, hazards, or cache config
WHY A GOLDEN MODEL HURTS
Reference simulators (Spike) are slow to run alongside RTL
They carry their own bugs — two implementations, which is right?
Impractical post-silicon: no internal observability on a real chip
THE TRADE-OFF THAT MATTERS
Handwritten suite
Low effort · no golden model · misses hazards
Random + golden model
Adapts · but slow, reference can be wrong
Formal verification
Complete · but poor scalability
PATARA (self-testing)
Adapts to implementation · NO golden model
11

## Slide 12
03 · BASE PAPER
Core Mechanism — REVERSI
12
THE KEY IDEA
You do not need to know the right answer — you only need the operation to be reversible.
Add 7, then subtract 7. If you do not land back where you started, the hardware is broken — and you never needed a reference model.
Rule: the instruction under test appears ONLY in the modification step — so a systematic fault cannot cancel itself out during restoration.
Fig. — REVERSI self-test structure (Gesper et al., 2026)
1 MODIFICATION
target = focus ⊕ random
apply the instruction under test
2 RESTORING
recovered = target ⊖ random
apply its inverse
3 COMPARISON
recovered == focus ?
mismatch → hardware error
12

## Slide 13
03 · BASE PAPER
Framework and Four Extensions
Each extension patches a specific blind spot the previous configuration leaves unreachable.
13
XML-driven flow
Processor + instruction set described in XML → selection → sequence generation → self-checking assembly. ISA-independent.
1 · Operand swapping
Focus is always operand 1, so operand 2’s forwarding path is never tested. Swapping reaches it.
2 · Hazard sequences
All instruction-type permutations, sequence length sized to pipeline depth (6 stages → 4 instrs).
3 · Cache-miss generation
Forces d-cache / i-cache misses to exercise stall × hazard interactions.
4 · TWIN-BASED CO-PROCESSOR VERIFICATION
Many co-processor operations (ABS, MIN/MAX, multiply) are not invertible, so REVERSI cannot apply. Instead the same operation runs on the co-processor AND as software on the already-verified RISC-V core, and the results are compared. The verified core becomes the golden model — no external reference, and it works post-silicon.
13

## Slide 14
03 · BASE PAPER
Experimental Results
DUT: 6-stage RV32IM core + V2PRO vector co-processor · Simulator: Questa Sim · Metric: code coverage (%)
14
Configuration
Instructions
Condition cov.
Compliance suite (baseline)
889,516
79.12%
Instruction combinations
6,983
80.21%
+ operand switching
9,722
81.31%
+ interleaving
17,294
81.31%
+ hazard sequences
1,851,852
96.70%
+ cache tests (full PATARA)
6,732,901
100.00%
KEY OBSERVATIONS
+20.88 pts condition coverage over the compliance suite
First config beats the suite with 127× fewer instructions
Interleaving alone adds 0.00 pts — variety ≠ coverage
ABLATION
Removing hazard-sequence generation drops condition coverage to 81.31%. The compliance suite found 0 bugs; PATARA exposed 4 categories of real hazard-interaction bugs.
14

## Slide 15
04 · APPLICATIONS
Applications and Relevance
15
WHAT IT ENABLES
Verifies a customized core the compliance suite cannot fully reach
Self-checking tests run post-silicon with no golden model
Twin method verifies an attached accelerator / co-processor
TRANSFERABLE INSIGHT
Separate the two questions: test generation vs. correctness oracle
When no golden model exists, invertibility or a twin can replace it
Coverage is necessary but not sufficient — 100% ≠ bug-free
RELEVANCE TO OUR PROJECT (TEAM 2)
We are extending a RISC-V core with custom AI / vector instructions for edge video anomaly detection — exactly the scenario PATARA targets.
Custom instructions have no golden reference — the paper’s core problem
Invertible ops (e.g. ADD+1) → REVERSI self-test directly
Non-invertible ops (e.g. packed abs-diff) → twin-based method
The accelerator we integrate maps onto the co-processor twin flow
Limitations: RV32IM only (no floating point) · CSRs and interrupts out of scope · single design evaluated.
15

## Slide 16
05 · COMPARISON
Comparison with Alternate Approaches
16
Paper
Approach
Strength
Main limitation
χRVFormal
High-level formal
Proves spec conformance; 7 real bugs
Bounded (depth 40)
Vector Accelerator
UVM + golden model
Industrial scale; 3,005 bugs; taped out
Code cov. only 72.6%
INSTILLER
Coverage-guided fuzz
Short tests; finds unthought-of cases
Incomplete; 2 non-RISC-V cores
PFV
BDD formal
Proven runtime bound; complete
Non-pipelined toy core
PATARA (base)
Self-testing
No golden model; 100% cov; post-silicon
RV32IM; no CSR / interrupts
WHY THE BASE PAPER WAS CHOSEN
PATARA is the only approach that verifies a customized RISC-V core without a golden reference — the exact obstacle our custom instructions create. It fuses systematic test generation, self-checking execution, and a twin-based co-processor method, and directly matches our project’s architecture and workflow.
16

## Slide 17
06 · CONCLUSION
Conclusion
17
Across the surveyed work, RISC-V verification splits along two axes — where tests come from, and how correctness is decided. Formal methods (χRVFormal, PFV) give complete guarantees but trade away either scalability or completeness; industrial UVM co-simulation (Vector Accelerator) and coverage-guided fuzzing (INSTILLER) scale to real cores but depend on a reference model and can never prove the absence of bugs. The base paper, PATARA, fuses systematic test generation with self-checking execution, removing the golden-model dependency entirely — reaching 100% condition coverage where the official compliance suite reached 79.12% and found no bugs, while exposing real hazard-interaction defects in that same design. For our project, where custom instructions have no golden reference by definition, this confirms self-testing and twin-based verification as the practical path forward — and points toward extending it to floating-point and privileged-mode coverage.
17

## Slide 18
07 · REFERENCES
References
18
[1] S. Gesper, F. Stuckmann, L. Wöbbekind & G. Payá-Vayá, "A Self-Testing Framework for Verification and Validation of a RISC-V-Based System with a Co-processor," Int. J. Parallel Programming, vol. 54, art. 15, 2026. (BASE PAPER)
[2] S. Shen, S. Chen, Y. Liu, L. Zhang, F. Song & Z. Wu, "χRVFormal: Formal verification of RISC-V processor Chisel designs," Journal of Systems Architecture, vol. 175, 103761, 2026.
[3] V. Jiménez et al., "Functional Verification of a RISC-V Vector Accelerator," IEEE Design & Test, vol. 40, no. 3, pp. 36–44, 2023.
[4] G. Zhang, P. Wang, T. Yue, D. Liu, Y. Guo & K. Lu, "INSTILLER: Toward Efficient and Realistic RTL Fuzzing," IEEE Trans. CAD of Integrated Circuits and Systems, vol. 43, no. 7, pp. 2177–2190, 2024.
[5] L. Weingarten, K. Datta & R. Drechsler, "Polynomial Formal Verification of a RISC-V Processor," IEEE Trans. on Nanotechnology, vol. 24, pp. 140–151, 2025.
[6] A. Waterman & K. Asanović, "The RISC-V Instruction Set Manual, Volume I: Unprivileged ISA," RISC-V International, 2019.
[7] E. Shazli & M. Tehranipoor, "REVERSI: Post-silicon validation via self-checking randomized test programs" (foundational REVERSI method extended by the base paper).
18